## Slide 1
Circuit & Systems Project | LTspice Simulation
AKSHAT KUMAR (12240080)
AYUSH KUMAR MISHRA (12240340)
Buck Converter Based EV Charging System

## Slide 2
  Objective: Design and simulate a DC-DC Buck Converter for EV/E-Bike battery charging.
  Converts 325V DC (rectified mains) to 48V DC.
  Target output current: 3A.
  Switching frequency: 50 kHz.
  Validate performance using LTspice transient simulation.
Introduction

## Slide 3
Simple and efficient method for voltage step-down.
High power efficiency (>90% achievable).
Smooth and stable DC output suitable for battery charging.
Why Buck Converter for EV Charging?
Lower switching losses and easier control technique.

## Slide 4
System Specifications

## Slide 5
  MOSFET ON → Inductor stores energy
  MOSFET OFF → Diode conducts, inductor releases energy
  Capacitor smooths ripple
  Output controlled by PWM duty cycle
Working Principle
AND
Circuit Diagram

## Slide 6
• PWM signal will be configured using the general form:
PULSE(V1, V2, Tdelay, Trise, Tfall, Ton, Tperiod)
• For this simulation: PULSE(0 10 0 10n 10n 2.96u 20u)
• Transient analysis will be performed using the general form:
.tran Tprint-step Tstop Tstart-save
• For this simulation: .tran 0 10m 5m
• Parameters to monitor: output voltage, inductor current, and switching waveforms.
LTspice Setup

## Slide 7
Simulation Results
  Output voltage settles near 48–55V
  Inductor current ~ 3A average
  Ripple visible due to switching
  Startup stabilization ~ 5 ms

## Slide 9
A 325V → 48V buck converter successfully modeled.
Suitable for low-power EV and E-bike charging systems.
Simulation validates correct operation and transient behavior.
Conclusion
MODEL
SUITABILITY
SIMULATION

## Slide 10
Applications
Small electric vehicle charging ports
Industrial DC supplies
E-bike battery chargers
UPS systems
Solar battery charging